## Slide 1: Java on Matlab
March 8th, 2017
Y.W. Chen

## Slide 2: Outline
Matlab Environment setting
JavaRobot Explanation
Issue Report

## Slide 3: Matlab Environment setting
In Matlab, Java version is depended on the install environment. To make sure the version of Java is concessive to the version of JavaRobot , type
  In the Command Windows
  version –java
  *Note that if your Java version is not the latest version, please use the uninstall tool here
  https://java.com/en/download/uninstalltool.jsp
  If the version you are using is not Java Runtime Environment 1.8.0_121 (aka 1.8.0_121-b13), then you may download it from the website or the link here:
  http://www.oracle.com/technetwork/java/javase/downloads/jre8-downloads-2133155.html
  Current computer is based on x64 structure, make sure you’ve downloaded the right file!s

## Slide 4: Under Windows Operation System
Step 1 : right click This PC  properties
Step 2 : go to Advanced system settings

## Slide 5: Under Windows OS
Go into the Environment variables
And create a system variable named MATLAB_JAVA with path variable
value of the jre file you’ve install

## Slide 6: Matlab Environment setting
If you still got some problem setting up the environment on other OS, the step is quite the same:
Check up Matlab Java version 
Download jre corresponding to the jre file we are using currently 
Add system environment variable called MATLAB_JAVA and its value of jre folder, etc. C:\Program Files\Java\jre 1.8.0_121
Restart Matlab and check version –java again
Notice that Matlab call method may be dysfunctional for other version of java file.

## Slide 7: JavaRobot Explanation
[JavaRobot, Tool, RefPosRMatrix] = JavaRobotRead();
  JavaRobot is an object representing the Robot, which be used in every function below.
  Tool store the original position data
  RefPosRMatrix  Reference Position Rotational Matrix
mThread = JavaRobotMove(Roll, Pitch, Yaw, speed, JavaRobot, Tool, RefPosRMatrix)
    mThread means the thread which will make sure the Robot’s moved to the target position
flag = mThread. isRobotMoveFinished()
  flag of Boolean 0 -> false(Not yet)/ 1 -> true(Done!)